## Slide 1: Environment Block Diagram
AXI4
P
AXI4
AXI4
S
axi4_master_1
axi4_slave_0
AXI4
axi4_master_0
axi4_slave_1
Class: axi4_2x2_fabric_qvip_environment Inst: qvip_env
Class: axi4_2x2_fabric_environment
DUT axi4_2x2_fabric
P
mvc_sequence_item_base
mvc_sequence_item_base
rw_txn
AXI4_MASTER_ID_WIDTH=4
AXI4_SLAVE_ID_WIDTH=5
S
P
P
S
P
S
P
Type: uvmf_in_order_race_scoreboard
Inst: axi4_txn_m1_sb
Type: axi4_rw_adapter
Inst: m0_rw_txn_pred
Class: slave_axi4_rw_adapter
Inst: slave_rw_txn_pred
Class: slave_axi4_txn_predictor
Inst: slave_axi4_txn_pred
Type: master_axi4_txn_adapter
Inst: m0_axi4_txn_pred
Type: uvmf_in_order_race_scoreboard
Inst: rw_txn_m0_sb
axi4_rw_transaction
Notes: This diagram shows the env for the axi4_2x2_fabric bench, including both the top level env and the sub env, qvip_env, the later which is the output from QVIP configurator. Note that all QVIP instances broadcast txn’s of type mvc_sequence_item_base. Then for demonstration purposes, there are two separate prediction + sb scenarios shown, with the top of the diagram regarding txn’s of type rw_txn and the bottom scenario regarding txn’s of type axi4_rw_transaction.
‘rw_txn’ is a generic type which is provided via QVIP AMBA adapter, as it converts AMBA protocol-specific txn’s such as AXI4, AHB, and APB to generic ‘rw_txn’ type for ease of prediction and comparison. The approach shown here for AXI4 can be utilized for any QVIP AMBA protocols.
The bottom scenario involves txn’s of type ‘axi4_rw_transaction’ which is specific to QVIP AXI4 txn’s. It’s use is demonstrated here as this same approach can be utilized for any txn type, be it AMBA, PCIe, Ethernet, I2c, etc. Namely casting the mvc_sequence_item_base to txn of protocol-specific type within user-defined predictor.

## Slide 2: Environment Block Diagram
AXI4
P
AXI4
AXI4
S
axi4_master_1
axi4_slave_0
AXI4
axi4_master_0
axi4_slave_1
Class: axi4_2x2_fabric_qvip_environment Inst: qvip_env
Class: axi4_2x2_fabric_environment
DUT axi4_2x2_fabric
P
mvc_sequence_item_base
mvc_sequence_item_base
rw_txn
AXI4_MASTER_ID_WIDTH=4
AXI4_SLAVE_ID_WIDTH=5
S
P
P
S
P
S
P
Type: uvmf_in_order_race_scoreboard
Inst: axi4_txn_m1_sb
Type: axi4_rw_adapter
Inst: m0_rw_txn_pred
Class: slave_axi4_rw_adapter
Inst: slave_rw_txn_pred
Class: slave_axi4_txn_predictor
Inst: slave_axi4_txn_pred
Type: master_axi4_txn_adapter
Inst: m0_axi4_txn_pred
Type: uvmf_in_order_race_scoreboard
Inst: rw_txn_m0_sb
QVIP UVMF UVM
axi4_rw_transaction
Notes: The same diagram as previous slide, the only difference being the components have been colored coded to discern their origin.
Note that the axi4_rw_adapter, in addition to the axi4 agents, are directly utilized from within the QVIP kit.
The scoreboards in use are provided as part of the UVMF base class libraries while the remaining components, for example the slave predictors, are user-customizable components derived from UVM components.
Showcasing that many different sources of components can be easily included and utilized within your UVMF bench.